Wood Norton Technical Areas
BNCS Documentation

Studio C Day to Day Routing Control Panel

Applcore Panel
BNCS Version 3 (Initial release)

Used in:
Studio A		✗
Studio C		✓
CTA		✗
CAR		✗
Vale Engineering Classrooms		✗
Bredon Wing		✗
Avon Wing		✗

Version	Edited by	Date	Key Changes
1	Andy Woodhouse	17/08/13	Initial release

# Background
Studio C has three routers within it's infrastructure:
1. Quartz SD-SDI – 128 sources, 128 destinations
2. Quartz Analogue Audio – 16 sources, 16 destination
3. AES/EBU audio – set in this application as 128 sources by 128 destination.
The Quartz units are standard hardware units.
The AES/EBU router is enabled as a ProBel control protocol within the Studer OnAir 3000 sound desk, and requires some configuration within the desk to map the logical inputs and bus outputs into BNCS sources, and to map the output stages of the desk to BNCS destinations. The BNCS control uses two BNCS database sets, one that provides the logical source and destination names, and one that records the (fixed) mapping between the Studer internal ProBel id and the external BNCS ID.
The three physical routers are combined through BNCS defined packages that enable a user to configure audio and video routes by the use of logical names. There are large numbers of logical sources and destinations (420 sources, 420 destinations).
The large size of the package names and crosspoints allows source and destinations to be grouped by function (eg VTR and Server), with many entries unused. For each source or destination package name there is an entry in the package crosspoints database of the form:
0124=23,13,29
Let us use this as a source package entry (database 0). The number to the left side of the equals sign indicates that the information is for source package 124, and the comma delimited list after the equals says that the package uses SDI input 23, analogue audio uses input 13, and the Studer AES/EBU logical source number is 29.
 A hyphen (-) indicates no crosspoint change is used for the element. For example a video only package may have an entry like “0129=72,-,-”.
The size of the package names and crosspoints is larger than that required for the normal day-to-day operation. The day-to-day operations use the first 360 sources and destinations. The sources and destinations from 361 are designated as “fixed” and editing their contents is a manual process. Such fixed entries are used to define hardwired combinations that should not be overridden by someone using the editor. An example of such a source is the camara inputs to the SDI router.
# Panel Function
Some signal routing tasks are more frequently needed than others – for example sending signals to the floor monitor displays. This panel supports that type of regular routing operation by providing the destination selections on simple to select panels. The active panel is chosen by a sub-panel select menu at the right hand side of the screen.
The sub-panels are:
1. Selection of the video signals to the soud check monitor and to the vision quality check monitor.
2. Panel two
3. Panel three
4. Panel four
5. Panel five
6. Panel six
7. Panel seven
8. Panel eight
9. Panel nine
# Dependencies
The panel requires ….
...a working CSI on the machine that runs the panel. Obviously for network updates the network and other work stations must also be active. Offline stations will collect updated driver INI files as part of their boot process.
## Significant Support Files
c:\bncs\ws_ini\wnglobal.ini	Names and numbers of drivers etc, read into memory at startup. / Also the names used for the source and destination packages are read from strings of the form StCSrcPkg and StCDstPkg in the [Matrix] section of the file.

For this panel the relevant driver INI files are:
dev_500.ini	Studio C Package names driver ID
dev_501.ini	Studio C SDI video driver ID
dev_502.ini	Studio C Analogue Audio driver ID
dev_503.ini	Studio C Digital Audio logical driver ID
dev_504.ini	Studio C Package Contents driver ID

dev_101.ini	CTA package names driver ID
dev_131.ini	CTA SDI router driver ID
dev_132.ini	CTA Analogue Audio router driver ID
dev_130.ini	CTA Package crosspoints driver ID
dev_100.ini	CAR Package names driver ID
dev_123.ini	CAR SDI router driver ID
dev_124.ini	CAR Audio router driver ID
dev_120.ini	CAR Package crosspoints driver ID

# Panels
There are multiple panels used in this task, all designed for use on a 1280 by 1024 pixel screen, with due allowance for the Studio C task selector bar at the bottom of the screen. There is a small headline bar at the top of the screen that shows the task name, the date, and the time. There is a sub-panel select menu bar at the right hand side of the screen.

# Variable Usage
Numeric memories
ID	Usage	ID	Usage
A%	Scratchpad	a%	Scratchpad used during crosspoint make
B%	Scratchpad	b%	Scratchpad used during crosspoint make
C%	Scratchpad	c%	Scratchpad used during crosspoint make
D%	Scratchpad	d%	Scratchpad used during crosspoint make
E%	Scratchpad	e%	Scratchpad used during crosspoint make
F%	Scratchpad	f%	Scratchpad used during crosspoint make
G%	Scratchpad	g%	Scratchpad used during crosspoint make
H%	Scratchpad	h%	Scratchpad used during crosspoint make
I%		i%	Scratchpad used during crosspoint make
J%		j%	Scratchpad used during crosspoint make
K%		k%	Scratchpad used during crosspoint make
L%		l%	Scratchpad used during crosspoint make
M%		m%	Scratchpad used during crosspoint make
N%		n%
O%		o%
P%		p%
Q%		q%
R%	Destination Number during revertive	r%
S%	Revertive numeric value	s%
T%		t%
U%		u%
V%		v%
W%	Database update – Router ID	w%
X%	Database update – Source/dest flag	x%
Y%	Database update – Index.	y%
Z%	Database update – Mapped ID	z%	Displayed panel number

String Memories
ID	Usage	ID	Usage
A$	Scratchpad	a$	Scratchpad used during crosspoint make
B$	Scratchpad	b$	Scratchpad used during crosspoint make
C$	Scratchpad	c$	Scratchpad used during crosspoint make
D$	Scratchpad	d$	Scratchpad used during crosspoint make
E$	Scratchpad	e$	Scratchpad used during crosspoint make
F$	Scratchpad	f$	Scratchpad used during crosspoint make
G$	Scratchpad	g$	Scratchpad used during crosspoint make
H$	Scratchpad	h$	Scratchpad used during crosspoint make
I$		i$
J$		j$
K$		k$
L$		l$
M$		m$
N$		n$
O$		o$
P$		p$
Q$		q$
R$		r$
S$	Revertive string value	s$
T$	Time	t$
U$	Date	u$	Colour – White text dark red background
V$		v$	Colour – Black text light red background
W$		w$
X$		x$	Colour – Yellow text dark blue background
Y$		y$	Colour – Yellow text light blue background
Z$		z$	Colour – Black text mid-grey background

# Numbered Memory Usage
### Integer Stores
Address	Content
1	Studio C SDI driver ID
2	Studio C Analogue Audio driver ID
3	Studio C AES-EBU Driver ID
4	Studio C Package Names Driver ID
5	Studio C Package Crosspoints Driver ID
6 … 10	Reserved, currently unused
11	CTA SDI driver ID
12	CTA Analogue Audio driver ID
13	Reserved in case ever have CTA AES-EBU Driver ID
14	CTA Package Names Driver ID
15	CTA Package Crosspoints Driver ID
16 / … / 20	Reserved, currently unused
21	CAR SDI driver ID
22	CAR Audio driver ID [Signal type defined by router output]
23	Reserved [in case ever have CAR AES-EBU Driver ID]
24	CAR Package Names Driver ID
25	CAR Package Crosspoints Driver ID
26 / … / 30	Reserved, currently unused
31 / … / 100	Unused
	Panel 1: 101 to 110 [Lip Sync Monitor Source, Precision Vision Monitor]
101	Source Bank Number
102	Source ID within bank
103	Source Package Crosspoint
104	Destination package ID
105	Source Selected flag
106	Destination Selected Ident – 0=none, 1=Sound, 2= Vision
107	---
108	---
109	---
110	---
	Panel 2: 111 to 120 [Multiviewer Assignable Inputs]
111	Source Bank Number
112	Source ID within bank
113	Source Package Crosspoint
114	Destination package ID
115	Source Selected flag
116	Destination Selected flag
117	Active Destination Button ID
118	---
119	---
120	---
	Panel 3: 121 to 130 [Mixer Inputs]
121	Source Bank Number
122	Source ID within bank
123	Source Package Crosspoint
124	Destination ID (matrix destination xpoint)
125	Source Selected flag
126	Destination Selected flag
127	TAKE enabled flag
128	TAKE Timeout counter
129	---
130	---
	Panel 4: 131 to 140 [Loop Devices]
131	Source Bank Number
132	Source ID within bank
133	Source Package Crosspoint
134	Destination ID (matrix destination xpoint)
135	Source Selected flag
136	Destination Selected flag
137	TAKE enabled flag
138	TAKE Timeout counter
139	Active Destination Button ID
140
	Panel 5: 141 to 150 [Wallbox Send]
141	Source Bank Number
142	Source ID within bank
143	Source Package Crosspoint
144	Destination package ID
145	Source Selected flag
146	Destination Selected flag
147	Active Destination Button ID
148	TAKE Enabled Flag
149	TAKE timeout counter
150	---
	Panel 6: 151 to 160 [CTA sources]
151	Source Bank Number
152	Source ID within bank
153	Source Selected flag
154	Destination Selected flag
155	Active Destination Button ID
156	CTA Destination Package ID
157	Video Layer enabled
158	Audio Layer enabled
159	TAKE Enabled Flag
160	TAKE timeout counter
	Panel 7: 161 to 170 [CAR Outside Sources]
161	Source Bank Number
162	Source ID within bank
163	Source Selected flag
164	Destination Selected flag
165	Active Destination Button ID
166	CAR Destination Package ID
167	Video Layer enabled
168	Audio Layer enabled
169	TAKE Enabled Flag
170	TAKE timeout counter
	Panel 8: 171 to 180 [Record Devices Inputs]
171	Source Bank Number
172	Source ID within bank
173	Source Selected flag
174	Destination Selected flag
175	Active Destination Button ID
176	CAR Destination Package ID
177	Video Layer enabled
178	Audio Layer enabled
179	TAKE Enabled Flag
180	TAKE timeout counter
	Panel 9: 181 to 190 [CTA Send]
181	Source Bank Number
182	Source ID within bank
183	Source Selected flag
184	Destination Selected flag
185	Active Destination Button ID
186	CAR Destination Package ID
187	Video Layer enabled
188	Audio Layer enabled
189	TAKE Enabled Flag
190	TAKE timeout counter
	Panel 10: 191 to 200 [CAR Send]
191	Source Bank Number
192	Source ID within bank
193	Source Selected flag
194	Destination Selected flag
195	Active Destination Button ID
196	CAR Destination Package ID
197	Video Layer enabled
198	Audio Layer enabled
199	TAKE Enabled Flag
200	TAKE timeout counter
	Panel 11: 201 to 210 [CCU to Camera SDI Router]]
201	Source selected flag
202	Active source button ID
203	Active source package ID
204	Destination selected flag
205	Active destination button ID
206	Active destination package ID
207	TAKE enabled flag
208	TAKE timeout counter
209
210

### String Stores
Address	Content
1 / … / 12	Names of Studio C source package groups, extracted from string StCSrcPkg= in c:\bncs\ws_ini\wnglobal.ini
13 … 20	Reserved, currently unused
21 … 32	Names of CTA source package groups, extracted from string CTASrcPkg= in c:\bncs\ws_ini\wnglobal.ini
33 .. 40	Reserved, currently unused
41 / … / 52	Names of CAR source package groups, extracted from string CARSrcPkg= in c:\bncs\ws_ini\wnglobal.ini
53 / … / 60	Reserved, currently unused
61 / … / 100	Unused
101 / … / 300	Studio C SDI revertive destination strings. First 128 locations hold strings of the form “7,711,” where the first number is the panel number to receive the source name, and 711 is the control ID. In theory could be multiple pairs present.
301 / … / 500	Studio C Analogue Audio revertive destination strings. / First 16 locations used
501 / … / 700	Studio C AES-EBU Audio revertive destination strings. / First 128 locations used.
701 / … / 900	CTA SDI revertive destination strings. / First 128 locations used.
901 / … / 1100	CTA Analogue audio revertive destination strings. / First 64 locations used.
1101 / … / 1300	CAR SDI revertive destination strings. / First 128 locations used.
1301 / … / 1500	CAR Analogue audio revertive destination strings. / First 128 locations used.

??? … 5000	Unused

# Applcore Code
It is assumed any person attempting to read this documentation is already familiar with general BNCS Applcore programming conventions such as line numbers used at startup and closedown of a panel.
Insert code here....